## Slide 1
Criticality Safety Evaluations (CSEs)
Jason M. Crye, PhD
NCS Engineer
Chris Haught
Chief NCS Engineer

## Slide 2: Outline
Purpose
Safety Criteria
Typical Steps
Other Considerations

## Slide 3: Purposes of Criticality Safety Evaluations
To demonstrate that the operation is adequately subcritical:
  under normal operating conditions
  under contingent (upset) conditions
To demonstrate that the operation meets ANSI/ANS-8.1 and -8.19 safety criteria
To derive limits and controls that ensure the above conclusions and bases are valid
To communicate to other analysts
To convince regulators that the above conclusions and bases are acceptable

## Slide 4
ONE BASIC SAFETY CRITERION From ANSI/ANS-8.1 (§4.1.2) and -8.19 (§7.1), Process Analysis (PA)
Before a new operation with fissionable material is begun, or before an existing operation is changed, it shall be determined that the entire process will be subcritical under both normal and credible abnormal conditions.

## Slide 5: Process Analysis (PA) Requirement
Abnormal conditions may include:
  A change in shape or dimensions
  Increase in mass of fissile material
  A change in concentration of fissile material in solution
  A reduction in the quantity of neutron absorber
  An increase in reflection
  An increase in interaction
  Physiochemical condition changes (boiling, precipitation, significant temperature reduction from cryogenic fluids, etc.)
Process Conditions: “The identifying characteristics of a process that have an effect on nuclear criticality safety”

## Slide 6: Process Analysis Requirement
All credible abnormal conditions?
  Identification of credible abnormal conditions is crucial
  Be aware that no process criticality accident occurred as a result of an erroneous calculation; many occurred as a result of a fault pathway that was not previously identified
  A thorough understanding of the process or activity is key to ensuring an adequate control set is developed
  A defense in depth philosophy is needed for prevention of nuclear criticality accidents
    More to follow on defense in depth

## Slide 7
NOTE: ANSI/ANS-8.1 does not define “credible” or other important terms
When ANSI standards use such terms without specific definition within the standard, the meaning of the terms is as defined by ordinary English usage (i.e., what Webster’s or other standard dictionary definitions state).
But “credible” is discussed in the new Appendix B…

## Slide 8: Process Analysis Requirement
How to apply credible?
Reconciling “credible abnormal conditions” with “economic considerations” and “protection of operating personnel and the public” is part of applying the Process A analysis requirement
    Cosmic impact? Major earthquake? Airplane crash?
“…relies on the judgment of the key professionals…”
“…can differ from process to process and site to site”
“Elimination of all risk is not possible”
Resources expended for NCS control should be commensurate with other hazards of similar consequences (paraphrased)

## Slide 9: Process Analysis Requirement
To meet the Process Analysis requirement:
Combinations of upset conditions should be considered.
  Rarely does occurrence of a single upset condition yield a criticality scenario. (Most criticality accidents result from multiple failures.)
  However, one event might affect multiple process conditions
  Examples: fire, violent chemical reactions, explosions, flood
If the combination of multiple upset conditions is credible and presents the possibility of a criticality accident, then the operation being evaluated does not meet the basic safety criterion of ANS-8.1 4.1.2.

## Slide 10
ANOTHER BASIC SAFETY CRITERION From ANSI/ANS-8.1, §4.2.2 Double-contingency Principle (DCP)
Process designs should incorporate sufficient
factors of safety to require at least two unlikely, independent, and concurrent changes in process conditions before a criticality accident is possible.

## Slide 11: Double Contingency Principle (DCP)
DCP does not limit changes in process conditions to only those that are considered credible
DCP does establish a lower limit on expected frequency of such changes: unlikely
  Typically considered once in 100 years (10-2 probability) or once in the lifetime of a facility
  What about changes in process conditions expected to occur more frequently?

## Slide 12: Double Contingency Principle
More on “Double”
    Not two contingencies! There will most likely be numerous upsets to consider.
    Not two controls! Maybe only a few NCS controls are needed. Maybe scores of controls are needed. This is determined by the analysis, not the Double Contingency Principle.
    Two layers of defense? Maybe two, maybe more. Again, determined by the analysis.
So, how many controls are needed?
  “…sufficient factors of safety…”

## Slide 13: Double Contingency Principle
Historically, regulatory agencies have required that “double contingency” be implemented as a requirement, without full understanding by regulation authors of:
  the original intent, or
  the difficulty in truly meeting double contingency for many categories of fissile operations.

## Slide 14: Double Contingency Principle
Why isn’t the Double Contingency Principle a requirement?
  There are situations where consequence mitigation minimizes the need for defense in depth (e.g. shielded facilities or underground tanks)
  Single barriers that are sufficiently robust (e.g. LEU UF6 cylinders)
  Credibility of a single change in process conditions (mass of a single HEU item)
  It is difficult if not impossible to verify (subjective rule)

## Slide 15: DCP Historical Perspective
LA-2063, 1956
LA-3366, 1964
…
is generally accepted as a guide to the
proper degree of protection against operational
abnormalities
that are improbable but
still cannot
be ignored. This rule calls for controls such
that no single mishap
can lead to a criticality
accident regardless of its probability of occurrence.
It is understood, further, that
there should
be protection against chains of related mishaps
and against combinations with other
abnormalities
that cannot be considered improbable. Obviously,
this rather subjective rule does little
more than
establish a point of view about criticality control
-
it cannot substitute for expert judgment,
e
xperience
and common sense usually provide the
only basis for classifying a conceivable mishap
as
“likely” or “unlikely,” or for ruling it out as
an impractical concept
…
.
The nuclear safety of any process will be
assured, wherever
p
ossible, by the dimensions of the components
-
such as pipe sizes
and container capacities
–
including
spacing between individual
components of the same or adjacent
systems. Where safety based on
geometry alone is precluded,
designs may be predicated on batch
sizes and/or
chemical concentrations, or combinations of them with
geometry,
and such designs will be considered satisfactory
only
if
two or more simultaneous an
d independent contingencies
must occur
to promote a chain reaction.

## Slide 16: DCP and Nuclear Parameters
DCP Require Multiple Parameter Control?
“Nuclear Parameters” – MAGIC MERV
DCP recommending control of at least two independent parameters has historically been an unofficial interpretation (i.e. not an official ANSI interpretation)
No longer required by DOE
ANSI/ANS-8.1 2014 version provides some clarification…

## Slide 17: DCP and Nuclear Parameters
DCP in ANS-8.1-2014, Appendix B
“…does not refer to parameters or controls…”
“The phrases ‘multiple controls on a single parameter’ or ‘multiple parameter control’ have no bearing on whether DCP is properly satisfied.”
The appendix suggests that crediting “multiple independent controls to prevent a single change in process conditions” is acceptable for complying with PA but not compliant with DCP
  DCP does not address credibility of “unlikely” changes

## Slide 18: My Perspective on DCP
Goals
  Defense in Depth
  Diversity of Controls (such that one change is not expected to affect all controls)
Practicality
  Control of two independent parameters may be effective for demonstrating subcriticality, but may lead to controls being out of balance with other similar hazards (safe mass and safe geometry?)
  Overall protection of the worker should guide application of DCP

## Slide 19: ANSI/ANS-8.19 Requirements
Requires PA
Credible abnormal determined with input from knowledgeable individuals
Evaluation determine/identify controlled parameters and their limits
Evaluation documented w/sufficient “detail, clarity, and lack of ambiguity” to allow for “independent judgment” of results
Reviewer familiar with NCS and operations

## Slide 20: ANSI/ANS-8.19 Recommendations
NCS staff performing evaluation observe relevant equipment, activities, and practices
Supervisor responsible for operation confirm normal and credible abnormal conditions; derived requirements are verifiable and compatible with operation

## Slide 21: Criticality Safety Evaluations (CSEs)
Normal
Conditions
Credible Abnormal
Conditions
Criticality
Accident
Possible
.
.
.
Contingencies
Must be unlikely, independent
(self-evident), and subcritical
.
.
.
Barrier Analysis
Typical PA
Whether or not documented,
analyst must understand where
criticality is possible

## Slide 22
Typical Process For Development of CSEs
Identify
Normal
Conditions
Identify
Contingent
Conditions
What can
go wrong?
"Normal"
may not
be typical
Neutronic
analysis
(calculations,
handbooks)
Limitations
on nuclear
parameters
How the
parameters
will be
controlled.
Understood?
Doable?
Evaluate
Conditions
Establish
Limits
Establish
Controls/
Requirements
Acceptance
by
Users
Evaluation
Approved
Implement
NCS Controls
Request made,
Understanding
Process/Activity
(See Note)
Note: this step is a formality; users should be involved during the development
Part Art, Part Science

## Slide 23: Request for NCS Evaluation
New or modified fissile material activity
Understand what is wanted
Understand what is needed
  Sometimes, wants ≠ needs (operational flexibility vs. convenient controls)
  Sometimes, wants and needs change while the evaluation is being developed.
Example
  Multiple batches in a glovebox with controls on # containers, spacing, lids on containers
  One batch at a time limited by fissile material mass

## Slide 24: Understanding the Process/ Activity
Most important step!
Research, Study, and Learn
  Material characteristics (physical, chemical properties)
  Process chemistry
  Material flows (incoming, outgoing, flow rates, waste streams, etc.)
  Material unaccounted for (normal and abnormal equipment holdup)

## Slide 25: Understanding the Process/Activity
Research, Study, and Learn
  Adjacent processes and operations (upstream, downstream, and lateral)
  Physical layout of equipment
  Function of the equipment
  Capability of the equipment

## Slide 26: Understanding the Process/Activity
Talk to operators, engineers, NCS analysts
Ask what can go wrong
Review safety analyses (e.g. ISAs and DSAs)
Inspect the field, observe operations
Pore over drawings, read procedures
  Become as knowledgeable as the system engineer

## Slide 27: Understanding the Process/Activity
Remember, no accident has occurred as a result of an erroneous calculation
Understanding the process/activity will provide a firm foundation for the NCS evaluation
Without such an understanding, your analysis is built on a house of cards

## Slide 28: Understanding the Process/Activity
Now that you understand the process…
Document a description of the process
  Include assumptions relevant to the evaluation
  Discuss inputs – fissile materials, chemical reagents, materials of construction, etc.
  Discuss product and waste streams

## Slide 29: Understanding the Process/Activity
Description of the process
  Discuss physical changes
  Discuss chemical reactions
  Present the boundaries of the system
  Discuss interfacing systems – ensure evaluations for these systems properly consider materials from your process
  Discuss utilities such as water, vacuum, or air

## Slide 30: Identify Normal Conditions
The Art –An Analytical Model of “Normal”
Normal conditions should bound actual conditions, plus…
  Including process upsets not considered to be unlikely (e.g. minor mass upsets)
  Including process variability (e.g. fissile solution concentration or powder density)
Ensure conservatism in NCS evaluation
  Gain practical flexibility in operations (e.g. no NCS controls on concentration or density)

## Slide 31: Why is a “normal” condition analysis needed?
Establish margin of safety.
In determining the normal condition is subcritical, the important operational and process characteristics that ensure subcriticality are defined.
  e.g. limited fissile mass, dryness, low fissile concentration, etc.
  Helps identify credible abnormal changes to the process/activity

## Slide 32: Identify Contingent Conditions
Unlikely Credible Abnormal Condition = Contingency
What can go wrong (e.g. excess fissile mass)
How can it go wrong (e.g. container overloaded)
To what extent it can go wrong (e.g. volumetrically full with some overflow)
  A contingency is not simply a control failure
      Important system attribute(s) must be affected
      Example: lid left off container

## Slide 33: Identify Contingent Conditions
The Art–Analytical Models for Contingencies
Understand basic routes/sequences leading from normal conditions to abnormal conditions
  This is why you should be as knowledgeable as the cognizant system engineer
  This is why other knowledgeable individuals should review
Identify what can go wrong in physical space, such as an addition of the wrong chemical reagent, operator inattention, process temperature too high, etc.

## Slide 34: Identify Contingent Conditions
Likelihood
  If a scenario does not meet your judgment for unlikely, it should be folded in with normal (e.g. small spill of fissile material)
  Credible extent of upset must be established (e.g. degree overmass or number of noncompliant containers in storage)
Beware of "single" events that affect multiple parameters and controls
  Flooding (reflection and moderation)
  Fire (physical damage plus flooding)

## Slide 35: Evaluate Conditions
The Science
NCS analysis – determining the system model is subcritical
  Comparative analysis to critical experiments or guides based on critical data
  Reference to nuclear safety guides and standards
  Hand calculations
  Computer code calculations (validated by comparison to critical experiments)

## Slide 36: Evaluate Conditions
Demonstrate normal conditions are subcritical
  Establishes controlled parameters
  Establishes margin of safety
Demonstrate contingent conditions are subcritical
  Satisfies PA
What if a contingent condition is not subcritical?
  additional controls must be established to preclude the possibility of a criticality accident (render scenario not credible; reduce degree of upset)

## Slide 37: Evaluate Conditions
The process/activity is understood in terms of physiochemical attributes such as weight, temperature, pressure, concentrations, flow rates, layout, capacities, etc.
Need a way to relate these attributes to what is evaluated for nuclear criticality safety…

## Slide 38: Evaluate Conditions
System attributesAnalysis Parameters
MAGIC MERV is the decryption key that opens the NCS analysis
  Identify parameters that must be controlled
  Understand how changes affect system reactivity
  Determine limitations on those parameters
  Meets intent of ANS-8.1 and -8.19 requirements and recommendations

## Slide 39: Establish Limits
Identify which parameter(s) need to be limited
  The value of the limit
  Limits must be within appropriate criteria for subcriticality (i.e. not exceed a subcritical limit or critical limit with margin applied)
  Criteria for calculated keff derived from validation

## Slide 40: Establish Controls/Requirements
Translate parameter limits from analysis back to the physical state
NCS requirements should be expressed using the same attributes by which the system is understood
  physical attributes such as weight, temperature, pressure, concentrations, flow rates, layout, capacities, etc.

## Slide 41: Establish Controls/Requirements
Three types of controls: 1) Passive engineered, 2) Active Engineered, 3) Administrative
Passive Engineered: Reliance should be placed on equipment design where dimensions are limited
  Most preferred per ANS-8.1
  LA-2063, 1956

## Slide 42: Establish Controls/Requirements
Active Engineered
  Uranium solution concentration monitor
    Programmed setpoint
    Interlocked to stop flow if setpoint is exceeded
Administrative (least preferred)
  Withdraw sample of solution
  Analyze for concentration
Be aware, administrative elements to maintaining engineered features

## Slide 43: Establish Controls/Requirements
Avoid impractical controls (e.g. mass limit where no means to weigh material).
Do not avoid controls for non-safety pressures.
Do not bias the type of controls for expediency (e.g. admin over new design feature)
Work with Operations counterparts to ensure the proposed requirements can be met
If controls are not convenient to follow, they will very likely be violated!

## Slide 44: Establish Controls/Requirements
Other Control Considerations
Nature of the operation vs. NCS control
  Chemical and physical properties of products
  ANSI/ANS-8.1 allows for credit of “natural or credible course of events”
  Examples: density of powder, H/X of material
Need for independent verification
  Compensate for sensitivity in the controlled parameter
Ability to recognize control failure
  Periodic surveillances
  Verification before beginning operation
  Not acceptable to remain unknown

## Slide 45: Establish Controls/Requirements
Apply additional defense in depth controls where judged appropriate for risk management
  Reduced operational limit where process does not require full allowance afforded by a subcritical limit
  Use of nuclear poisons where practical (e.g. borosilicate glass equipment)

## Slide 46: Thoughts on Conservatism
Include conservatism where feasible:
  To account for real-world uncertainties.
  To simplify modeling.
  To meet facility/site safety policies (e.g. optimum moderation, full enrichment).
Beware of unintended consequences:
  May hinder operations, restrict productivity, or cause other safety problems.
  May result in confusing requirements being imposed on operations personnel
  May encourage shortcuts

## Slide 47: Acceptance by Users
The operating organization is ultimately responsible for safety
The NCS analyst must clearly explain the intent of the controls
The operating organization must
  Validate the controls can be met
  Identify how controls will be implemented and maintained

## Slide 48: Other Considerations for Evaluation
Criticality accident alarm system coverage
Access to references and supporting NCS calculations
Document control and record retention
Interface with regulatory oversight
Interface with facility safety documentation
  Consistency with safety analysis
  Elevation of NCS controls (i.e. ISAs or DSAs)