## Slide 1
NCS Code Validation
ANSI/ANS-8.24
Chris Haught
Chief NCS Engineer for Consolidated Nuclear Security, LLC

## Slide 2: Outline
Purpose
Requirements
Issues
Process to determine upper subcritical limit
Examples

## Slide 3: Purpose
Validation is defined as “The process of quantifying … the suitability of a computer code system for use in nuclear criticality safety analyses…”
To establish the adequacy of a computer, code, and cross section set
(“the computational method”) for its intended use,
AND
To quantify the calculational bias and uncertainties, and acceptance criteria such that there is confidence that the calculated results thought to indicate subcriticality reliably indicate subcritical systems.
Different from “verification”, which establishes that your code is installed correctly and tests functionality issues
An upper subcritical limit (USL) is determined through the validation effort

## Slide 4: Basic requirements from ANSI/ANS-8.24
ANSI/ANS-8.24, Validation of Neutron Transport Methods for Nuclear Criticality Safety
Select benchmarks
Determine calculational bias
Determine uncertainties in the bias
Establish a margin of subcriticality
Establish the validation area of applicability
Document work and conclusions

## Slide 5: Benchmarks
“A representation of an experiment evaluated for use in validation. The experiment may be critical or slightly subcritical…”
These are the experiments defined in sufficient detail to create an accurate model of the experimental setup
Experiments involving materials and configurations similar to the actual fissile material processes at the site where the validation is applied
Should select as many experiments available that are similar to the actual fissile material processes
  Typically > 100
Validation must also consider the conditions representing the credible abnormal conditions associated with the fissile material processes
  Credible abnormal conditions are identified in the NCS Evaluations for the processes

## Slide 6: Area of Applicability
Also referred to as validation applicability
“A domain, which could be beyond the bounds of the benchmark applicability, within which the margins derived from validation of a calculational method have been applied”
Benchmark applicability is the range of benchmark parameters (e.g., material compositions, geometry, neutron energy spectra) over which the bias and bias uncertainty of a calculational method are established.
Allows for extrapolation and wide interpolation of benchmnark data

## Slide 7: Area of Applicability
Examples
Fissile Material Composition
  Uranium (high or low enriched)
  Plutonium (high or low 240Pu content)
  Solid or liquid (density/concentration)
  Metal or compounds (oxides, nitrates, etc.)
  Moderation (dry, water, carbon, Be, etc.)
  Homogeneous or heterogeneous
Neutron energy
Neutron absorbers
Geometry configuration
Single unit or interacting units (arrays)
  Interspersed materials
Reflected or unreflected

## Slide 8: Area of Applicability
Can also be characterized in terms of physical or nuclear parameters with numerical limits
Examples -
Moderator ratio (H/X = 10 to 1000)
Average energy group (AEG = 6.5 to 21.3)
Energy at average lethargy (E = 0.025 to 300 keV)
Uranium Concentration (50 to 200 g-U/L)
Enrichment (2 to 10%)

## Slide 9: Bias
A measure of the systematic difference between the experimental data (benchmark cases) and the calculated results.
Bias may not be constant; it may be a function of one or more independent variable(s) due to trends.
An experiment has a measured keff of 1.000, the calculated keff of the benchmark model is 1.003, the deviation for that case is 0.003.
These individual deviations are used to compute the systematic bias

## Slide 10: Bias
Bias is estimated for a group of benchmark results
Can be represented by regression analysis or by the average,
  Supplemented by visual inspection

## Slide 11: Bias Uncertainty
“Accounts for the combined effects of uncertainties in the benchmarks (i.e. critical experiment), the calculational models of the benchmarks, and the calculational method”
The critical experiment uncertainties include:
  Material specifications - fuel and hardware (composition, assay, mass, density, etc.).
  Dimensional specifications - fuel and hardware (experimental apparatus, surroundings, etc.)
  Experimenters' manipulation and adjustments to the reported data.
The calculational model uncertainties include:
  Geometric modeling used
  Code options used (e.g. histories and generations, S(α,β), albedos, etc.).

## Slide 12: Bias Uncertainty
The calculational method uncertainties include:
  Convergence criteria (deterministic codes) or statistical variation (Monte Carlo codes) (usually negligible).
  The mathematical equations solved and approximations used.
  Cross-section data and scientists’ evaluation of that data (ENDF libraries).
  Resonance cross section processing
The combined uncertainty is exhibited as scattering of the calculated results
Typically quantified using statistical analysis

## Slide 13: Errors
Not part of the bias uncertainties
ANSI/ANS-8.24 requires independent review of:
  the benchmark applicability
  the input files and output files to ensure accurate modeling and adequate convergence
  the methodology, and its use, for determining bias, bias uncertainty, and margins
  concurrence with the validation applicability (interpolation between benchmarks and extrapolation)
The value of the upper subcritical limit (kUSL) is never intended to compensate for errors!

## Slide 14: Margin of Subcriticality
“An allowance beyond the calculational margin to ensure subcriticality”
Calculational Margin: An allowance for bias and bias uncertainty plus considerations of uncertainties related to interpolation, extrapolation, and trending
Also called the minimum subcritical margin
Think of this margin of subcriticality as bolstering confidence in the upper subcritical limit
Typically includes between 2 and 5% Δk (i.e. 0.02 to 0.05) that is best described as commonly accepted “good practice”
  A value of 2% ΔK is not unusual within the DOE complex

## Slide 15: Margin of Subcriticality
What does it cover?
  The origins of the MoS values in use are not clear
  Some say it is there to cover the “unknown unknowns”
What is NOT covered?
  Does not cover any accident or upset condition
  Does not cover software or data error
  Does not cover poorly characterized system models

## Slide 16: Upper Subcritical Limit
kUSL = 1.0 + Bias - Bias Uncertainty – MoS
This is the maximum allowable keff accepted as being subcritical, with some defined confidence
1.0 represents the experimental result
Bias: estimate of expected difference between computed and experimental results
  Must be estimated over the entire domain representing validation applicability
  Can be a constant or a function
Bias Uncertainty: uncertainty in the bias estimate
  Typically determined by the variability in the benchmark results (residuals between bias estimate and computed keff)
  Can be a constant or a function
MoS: margin of subcriticality
  Typically a constant
This form does not include margin for wide
interpolation or extrapolation

## Slide 17: Upper Subcritical Limit
Typical acceptance criterion:
keff + 2scalc ≤ kUSL
In order for a calculated configuration to be considered (reliably) subcritical, the computed keff, including calculational uncertainty, must not be greater than the USL
This does not necessarily represent a safe fissile material process
It merely represents a condition that is reliably subcritical – provided no other changes to the system occur
The NCS evaluation determines the fissile material process is safe

## Slide 18: Validation Report
Description of the critical experiments
  Materials
  Dimensions
  Other parameters used to establish applicability
Description of the calculational models
  Differences between experiments and models
Description of the calculational method
  Code (e.g. MCNP or SCALE) and version
  Platform (i.e., the machine on which the code is installed)
  Calculational technique (e.g. kcode or CSAS25)
  What cross section set was used
  Cross section processing options used (e.g. S(α,β) or NITAWL resonance processing)
  Other code options

## Slide 19: Validation Report
Description of the validation technique
  Range/area of applicability
  Determination of bias, bias uncertainty
  Margin of subcriticality
  Extrapolation and wide interpolation (if allowed) and additional margin to apply
  kUSL

## Slide 20: Validation Report
Pedigreed descriptions of numerous critical experiments are available in The International Handbook of Evaluated Criticality Safety Benchmark Experiments
Commonly referred to as the ICSBEP – International Criticality Safety Benchmark Experiment Project
Validation reports typically reference the handbook for benchmark details

## Slide 21: Issues
“A positive bias exists where the mean bias or the value of the fitted function is greater than zero”
This is where the mean keff is greater than 1 or the range where the keff function is greater than 1
If positive bias is used, “…its use shall be justified by the close applicability of the benchmarks.”
“If the justification cannot be made, the positive bias shall be removed using methods consistent with the statistical approach or through the use of an increased margin of subcriticality”
Not all “critical” experiments have keff of 1
Benchmark results can be normalized for statistical analysis:

## Slide 22: Issues
“The margin of subcriticality and its basis shall be documented.”
  The origins of the MoS values in use are not clear
  Some say it is there to cover the “unknown unknowns”
Adequacy of cross section data for certain materials
How close does the system of concern need to "fit" the range of applicability?
Use of benchmarks that have been used to evaluate nuclear data
  Computed keff should be exactly 1 because the nuclear data was adjusted to achieve that result
Are statistical processes even applicable?
  Each critical experiment is a unique measurement involving specific materials, configurations, and conditions. Statistics views experiments (i.e. a sample population) as a common effort to measure the “same” condition (keff = unity.)

## Slide 23: Statistical Analysis
Typically used to determine bias and bias uncertainty
Population:
  the actual or sample population (seen)
  and
  the true or parent population (not seen)
The actual or sample population is the set of calculated keff values for the set of experiments utilized (i.e. benchmark cases)
The true or parent population is the statistical extension of the observed population to a hypothetical infinite number of experiments within the area of applicability

## Slide 24: Statistical Analysis
Deviation: the difference between an individual sample point and the estimate determined from all sample points
Variance:
  Average of the squares of the deviations about the sample mean (divide by N-1)
  or
  Average of the squares of the deviations about keff(x) correlation (divide by N-2 for first order fit)
Standard Deviation: The square root of the variance for a normal (Gaussian) distribution
Confidence Level: the percentage of all possible samples that can be expected to include the true population parameter
Benchmark Uncertainty
  Can be used for weighting

## Slide 25
A decision process for selecting a statistical method to compute bias and bias uncertainty
(1.0 + Bias - Bias Uncert)
Least
conservative
Most
conservative
Consider what the
desired area of
applicability is

## Slide 26: Selecting a Statistical Method
Confidence and tolerance bands will follow the curve fit (below the fit)
Confidence band may not lie below all data points
Tolerance limit lies below the average

## Slide 27: Non-parametric Method (NUREG/CR-6698)
Used when sample population does not have a normal distribution (or another distribution with defined parameters)
(above the value at rank m)

## Slide 28: Non-parametric Method (NUREG/CR-6698)
(1.0 + Bias - Bias Uncertainty)
(above the lowest rank)

## Slide 29: Non-parametric Method (NUREG/CR-6698)

## Slide 30: Single-sided Lower Tolerance Limit
A single, lower limit above which a defined fraction of the true population of calculated keff values are expected to lie with a prescribed confidence within the area of applicability
The limit is computed from the mean of the results
95% confidence and 95% population fraction are typical

## Slide 31: Single-sided Lower Tolerance Limit (NUREG/CR-6698)
(1.0 + Bias - Bias Uncertainty – MoS)
Applicability: Sample data (benchmark keff’s) must be normally distributed
  Must test for normality – many acceptable statistical methods are available
U is the one sided lower tolerance factor
SP is the square root of pooled variance

## Slide 32: Single-sided Lower Tolerance Limit (NUREG/CR-6698)
Selection of single-sided lower tolerance factor, U
If data points (benchmark experiments) exceed 50, the factor for n=50 may be conservatively used

## Slide 33: Single-sided Lower Tolerance Limit (NUREG/CR-6698)
Mean and Pooled Variance – Nonweighted
Mean (average) keff:
n is the number of data points
Variance about the mean:
(square root of) Pooled variance:
  Only considers variability in results and not benchmark uncertainties

## Slide 34: Single-sided Lower Tolerance Limit (NUREG/CR-6698)
Pooled Variance – Weighted Formulations
Weighted against benchmark uncertainty
Weighted variance about the mean:
Average total uncertainty:
Weighted average keff:

## Slide 35: Single-sided Lower Tolerance Limit (NUREG/CR-6698)
Pooled Variance - Weighted Formulations, continued
Square root of pooled variance:
For non-weighted application, keff is the mean, σ2 is zero, and pooled variance reduces to variance about the mean

## Slide 36: Single-sided Lower Tolerance Band
A band about a keff correlation above which a defined fraction of the true population of calculated keff values are expected to lie with a prescribed confidence
A tolerance band requires a regression fit to the data
The fitted curve lower-bounds the "true" keff population
Limited extrapolation beyond the benchmark applicability is reasonable

## Slide 37: Single-sided Lower Tolerance Band (NUREG/CR-6698)
Method based on establishing a trend with some independent variable (e.g. H/X, fissile constituent concentration, average energy group, etc.)
Calculated keff’s are fitted to a line or curve as a function of that independent variable
Some type of Goodness of Fit test is necessary to establish a valid trend
  Chi-squared
  Correlation coefficient (R2)
  Visual observation
  Many others
If there is not a good fit, then this method cannot be used

## Slide 38: Single-sided Lower Tolerance Band (NUREG/CR-6698)
Bias is represented by fit to keff results - Kfit(x)
Pooled variance, SPfit, is determined for fit to keff results
  Measures spread of results
  (more to follow)
Factors inside the brackets measure the spread of the independent variable
  (more to follow)
KL = (1.0 + Bias - Bias Uncertainty)

## Slide 39: Single-sided Lower Tolerance Band (NUREG/CR-6698)

## Slide 40: Single-sided Lower Tolerance Band (NUREG/CR-6698)
Pooled Variance - Unweighted
Variance:
Square root of pooled variance:
Pooled Variance - Weighted
n-2 for a linear fit
Terms to be replaced
in KL formulation

## Slide 41: Single-sided Lower Tolerance Band (NUREG/CR-6698)
Pooled Variance – Weighted, continued
Average total uncertainty:
Variance:
Square root of pooled variance:
n-2 for a linear fit

## Slide 42: Single-sided Lower Confidence Band
A band about a keff correlation that lower bounds the true correlation with a prescribed degree of confidence (the fitted curve lower-bounds the bias and accounts for uncertainty of the bias)
A confidence band requires a regression fit to the data
Limited extrapolation beyond the benchmark applicability is reasonable
Least conservative among the four methods
Requires practitioner judgment for its usage plus choice of MoS

## Slide 43: Single-sided Lower Confidence Band
The lower confidence band formulation for KL is the same as the lower tolerance band but with the last term omitted
All other terms and formulations presented for the lower tolerance band apply to the lower confidence band
KL = (1.0 + Bias - Bias Uncertainty)
Omission of this term results in the confidence band formulation

## Slide 44: Examples
Lower tolerance limit
Nonparametric limit
Lower confidence band

## Slide 45
EXAMPLE 1: Lower Tolerance Limit
Code and cross section, computer:
KENO-V.a as SCALE 4.4a routine CSAS25,
ENDF/B-V – based 238-neutron-energy group library
WS5, a controlled and verified workstation at ORNL

## Slide 46
EXAMPLE 1: Lower Tolerance Limit
Code Options:
“Latticecell” for cross-section processing.
Standard specifications for the KENO-V.a case inputs included:
GEN=550 (number of generations)
NPG=10,000 (number of neutrons per generation)
NSK=50 (number of generations to skip)
SCT=3 (order of scattering, P5)
In general, each KENO-V.a result is based on ~5,000,000 neutron histories.
Flat neutron start, no albedos or reflector biasing options used.

## Slide 47
EXAMPLE 1: Lower Tolerance Limit
Selected Benchmark Experiments:
The LEU-COMP-THERM-001 experiments had square-pitch lattices of 2.032 cm, and a 235U enrichment of 2.35 %. In one experiment, all involved fuel rods were in a single cluster. In the remaining seven experiments, the rods were arranged in three separate clusters, with spacing between the clusters ranging from ~4 cm to ~ 12 cm.
The LEU-COMP-THERM-002 experiments had square pitch lattices of 2.54 cm and a 235U enrichment of 4.31 %. The experimental material was obtained from N. S. Savannah Core II fuel assemblies; the fuel pellets were of the same diameter as for the lower enrichment (3.9%) Core II fuel.
The LEU-COMP-THERM-007 experiments involved a 235U enrichment of 4.738 %. Both square and triangular lattices were involved, with fuel rod pitches varying from 1.26 cm to 2.52 cm.

## Slide 48
EXAMPLE 1: Lower Tolerance Limit
Selected Benchmark Experiments: (Cont’d)
The LEU-COMP-THERM-009 experiments involved a 235U enrichment of 4.31 %, using the same experimental rods as for LEU-COMP-THERM-002, in clusters of three fuel rod lattices similar to those considered in LEU-COMP-THERM-001. In the LEU-COMP-THERM-009 experiments, absorber plates of various materials were located between the two outer clusters and the central cluster. Square lattices of 2.54 cm pitch were involved. Only the first four experiments were selected for inclusion in this validation; those experiments involve mild steel plates of 0.485 cm (0.191-inch) or 0.302 cm (0.119-inch) thicknesses as the absorber plates.
The LEU-COMP-THERM-019 experiments involved a 235U enrichment of 5.00 %. Three experiments in triangular lattices were involved, with fuel rod pitches of 0.7, 0.8 and 1.4 cm. These experiments are distinct from the other experiments utilized here, in that the fuel rods are fabricated using stainless steel as the cladding. (All other referenced ICSBEP low-enrichment fuel reports involve aluminum-clad fuel.)

## Slide 49
EXAMPLE 1: Lower Tolerance Limit
Benchmark
Results:
(30 points)

## Slide 50
EXAMPLE 1: Lower Tolerance Limit
No obvious or significant trend in data if stainless steel clad experiments are omitted.
Apply Shapiro-Wilk test for normality to the 27 points (with stainless clad experiments omitted).
NOTE: Normality test fails with stainless steel clad experiments included, as expected.

## Slide 51
EXAMPLE 1: Lower Tolerance Limit
Terms for Shapiro-Wilk Normality Test

## Slide 52
EXAMPLE 1: Lower Tolerance Limit
Processing of 27
Data Points
Notes: S2 is the sum of the squares of the deviation, not the variance

## Slide 53
EXAMPLE 1:
Lower Tolerance
Limit
Application of
Shapiro-Wilk Test
for Normality of
Data

## Slide 54
EXAMPLE 1: Lower Tolerance Limit
Determination of USL (kUSL):
KUSL = keff – USp – MoS
(1.0 + Bias - Bias Uncertainty – MoS)
U is the one sided lower tolerance factor
Sp is the square root of pooled variance
Use a MoS = 0.02.
Notes: KsubL is the limit with bias and bias uncertainty

## Slide 55
EXAMPLE 1: Lower Tolerance Limit
Determination of SP , weighted factors:
Datapoint uncertainty
Variance about the mean
Average total uncertainty
Similar terms apply for non-weighted application.
(σi)

## Slide 56
EXAMPLE 1: Lower Tolerance Limit
Determination of SP , weighted factors (cont’d):
Weighted average keff
Square root of pooled variance
For non-weighted application, keff is the mean, 2 is zero,
Pooled variance reduces to variance about the mean

## Slide 57
EXAMPLE 1: Lower Tolerance Limit
Determination of USL (kUSL)
(Nonweighted Example)
Notes: Sp2 is the sum of the squares of the deviations divided by n-1

## Slide 58
EXAMPLE 2: Non-Parametric Limit
Need: A kUSL value for highly enriched uranium as single or multiple units, in well-moderated forms (i.e., mixed with water).
In the process application, moderating reflectors of concern are water or concrete (or both).

## Slide 59
EXAMPLE 2: Non-Parametric Limit

## Slide 60
EXAMPLE 2:
Non-Parametric Limit
Picked many highly
enriched uranium
(HEU) solution
experiments…

## Slide 61
EXAMPLE 2: Non-Parametric Limit

## Slide 62
EXAMPLE 2: Non-Parametric Limit
Check for Fit as Function of AEG

## Slide 63
EXAMPLE 2: Non-Parametric Limit
Check for Fit as Function of EALF

## Slide 64
EXAMPLE 2: Non-Parametric Limit
Check for Fit as Function of H:235U Ratio

## Slide 65
EXAMPLE 2: Non-Parametric Limit
Check for Fit as Function of Nitrate Content

## Slide 66
EXAMPLE 2: Non-Parametric Limit
Check for Fit as Function of 235U Concentration

## Slide 67
EXAMPLE 2: Non-Parametric Limit
Qualitative Check

## Slide 68
EXAMPLE 2: Non-Parametric Limit
90 Cases Fail Chi-Square Normality Test (Dk=0.004)

## Slide 69
EXAMPLE 2: Non-Parametric Limit
Fails Chi-Square Normality Test Again (Dk=0.002)

## Slide 70
EXAMPLE 2: Non-Parametric Limit
Guidance from NUREG/CR-6698
(above the value at rank m)

## Slide 71
EXAMPLE 2: Non-Parametric Limit
Guidance from NUREG/CR-6698
(1.0 + Bias - Bias Uncertainty)

## Slide 72
EXAMPLE 2: Non-Parametric Limit
Application
There are n = 90 data points.
The confidence level that 95% of similar critical systems will have computed keff values greater than the lowest computed keff value is
= 1 – qn = 1- (0.95)90
= ~ 99%

## Slide 73
EXAMPLE 2: Non-Parametric Limit
Our degree of confidence is ~ 99% (for 95% of the population); an NPM value of 0.0 is appropriate.

## Slide 74
EXAMPLE 2: Non-Parametric Limit
Lowest computed keff value is 0.9913,
with scalc = 0.0005 and sexpt = 0.0025;
total = 0.00255.
kUSL = smallest keff value
- uncertainty of smallest keff value
- non-parametric margin
- MoS
kUSL = 0.9688 for MoS = 0.02.

## Slide 75
EXAMPLE 3: Lower Confidence Band
Equations are more complicated, especially if data uncertainty (weighted values) are used. From NUREG/CR-6698:
Note: Omission of this term results in the confidence band fit
(1.0 + Bias - Bias Uncertainty)

## Slide 76
EXAMPLE 3: Lower Confidence Band

## Slide 77
Bias is represented by fit to keff results
  First order least squares in this example
  Trial and error
Pooled variance is determined for fit to keff results
  Measures spread of results
  Weighted formulation includes avg. total uncertainty, 2
  Factors inside the brackets measure the spread of the independent variable
EXAMPLE 3: Lower Confidence Band

## Slide 78
EXAMPLE 3: Lower Confidence Band
All 76 thermal and epithermal 233U solution benchmarks in the 2001 IHECSB Handbook: keff vs AEG

## Slide 79
EXAMPLE 3: Lower Confidence Band
All 76 thermal and epithermal 233U solution benchmarks in the 2001 IHECSB Handbook: keff vs EALF

## Slide 80
EXAMPLE 3: Lower Confidence Band
All 76 thermal and epithermal 233U solution benchmarks in the 2001 IHECSB Handbook: keff vs 233U Concentration

## Slide 81
EXAMPLE 3: Lower Confidence Band
All 76 thermal and epithermal 233U solution benchmarks in the 2001 ICSBEP Handbook: keff vs H:233U atom ratio

## Slide 82
EXAMPLE 3: Lower Confidence Band
All 76 thermal and epithermal 233U solution benchmarks in the 2001 IHECSB Handbook: keff vs NO3 content

## Slide 83
EXAMPLE 3: Lower
Confidence Band
Final confidence
band expression
(MSM is MoS)
(1.0 + Bias - Bias Uncertainty)

## Slide 84
EXAMPLE 3: Lower
Confidence Band
Final confidence
band tabulated
values
(MSM is MoS)

## Slide 85
EXAMPLE 3: Lower Confidence Band

## Slide 86
EXAMPLE 3: Lower Confidence Band
Area of Applicability Statement

## Slide 87: Essential References
NUREG-1475, Revision 1, “Applying Statistics,” 2011
NUREG/CR-6698, "Guide for Validation of Nuclear Criticality Safety Calculational Methodology," 2000.
FCSS ISG-10, Nuclear Regulatory Commission Interim Staff Guidance 10, "Justification for Minimum Margin of Subcriticality for Safety," 2006.