## Slide 1
Hand Calculations
Chris Haught
Chief NCS Engineer for Consolidated Nuclear Security, LLC

## Slide 2: Outline
Learning Objectives
Purpose
Overview of Hand Calculation Primer
Confidence in Methods
Single Unit Methods
Array Methods

## Slide 3: Learning Objectives
Learn some of the hand calculation methods discussed in the Hand Calculation Primer, LA-14244-M
  Available on the web
Hand calculations methods are required training for Nuclear Criticality Safety (NCS) engineers per ANSI/ANS-8.26-2007, §7.2 “Methods”
Hand calculations to be discussed here:
  Single Unit Methods
    Fraction Critical
    Core density conversions
    Diffusion Theory (Buckling)
  Array Methods
    Surface density
    Density analog
    Limiting surface density
    Solid angle

## Slide 4: Purpose of Hand Calculations
Learning these methods can provide insight to new NCS personnel developing intuition, knowledge and experience in the field
  Gain insight into the physics of fissile systems
Hand calculations can be very effective tools
  Support for NCS evaluations
  Easily adapted to scripts, spreadsheets or programming languages for use in parametric studies
  Starting point for more complex calculations
  Useful as a “sanity check” for a code calculation result
  Helpful in response to abnormal conditions

## Slide 5: Hand Calculation Primer
Extrapolation Distance
Fraction Critical

## Slide 6: Hand Calculation Primer
Each hand calculation method in the Primer (Chapters 2 through 8) is organized as follows
  “What you will be able to do”
  Method overview
  Method applicability
  Example problem solutions (except solid angle)
  Verification of example problem solutions using a code package or other result is provided in Chapter 9

## Slide 7: Confidence in Hand Calculations – Single Unit Methods
Problem:
  The Godiva I critical assembly at Los Alamos was used to perform various critical experiments. Assume the assembly is made from 93% enriched 235U (density: 18.8 g/cm3) and is essentially an unreflected system.
  Using one-group diffusion theory, estimate the spherical critical radius for this system when the three fissile pieces are fully assembled.

## Slide 8: Confidence in Hand Calculations – Single Unit Methods (Cont.)

## Slide 9: Confidence in Hand Calculations – Array Methods
Problem:
  HEU-MET-FAST-023 Case 22 (ICSBEP Handbook), 4x4x4, 10.5 kg U Metal (93.2), 15.2 cm Paraffin Reflector.
Using the following array methods, verify the center-to-center spacing between the array units.
  Surface density method
  Density analog method
  Limiting surface density method

## Slide 10: Confidence in Hand Calculations – Array Unit Methods

## Slide 11: Single unit methods
Fraction Critical
Core Density Conversion
Diffusion Theory (including buckling)

## Slide 12: Multiplication Factor Vs. Fraction Critical
The fraction critical may be used to determine the approximate multiplication factor of a single unit
Fraction critical, f
  Defined as the ratio of the mass to the critical mass of the same material with the same reflection conditions:

## Slide 13: Multiplication Factor Vs. Fraction Critical
  For instance, the critical mass of a bare sphere of a-phase 239Pu metal is 10.3 kg
  A bare sphere consisting of 4.5 kg of a-phase 239Pu metal has a fraction critical of:

## Slide 14: Multiplication Factor Vs. Fraction Critical
  The critical mass of a water-reflected sphere of a-phase 239Pu metal is 5.4 kg
  A water-reflected sphere consisting of 4,500 g of a-phase 239Pu metal has a fraction critical of:

## Slide 15: Multiplication Factor Vs. Fraction Critical
The following figures show the keff’s as a function of the fraction critical for several spherical materials, both bare and water-reflected
The solid line included is an empirical formula approximating the keff for each f

## Slide 16: Multiplication Factor Vs. Fraction Critical
LA-14244-M, Appendix B

## Slide 17: Multiplication Factor Vs. Fraction Critical
LA-14244-M

## Slide 18: Multiplication Factor Vs. Fraction Critical
LA-14244-M

## Slide 19: Multiplication Factor Vs. Fraction Critical
For fast systems, both bare and reflected, a reasonable approximation of keff can be made using the following formula:
For thermal systems, a reasonable approximation of keff can be made using the following formula:
  Can also be used for arrays of similar units if the critical mass of a unit in the array is known

## Slide 20: Multiplication Factor Vs. Fraction Critical
  The critical mass of a bare sphere of a-phase 239Pu metal is 10.3 kg
  A bare sphere consisting of 4.5 kg of a-phase 239Pu metal has a fraction critical of:
What is the keff of the 4.5-kg 239Pu bare sphere?

## Slide 21: Multiplication Factor Vs. Fraction Critical
  The critical mass of a bare sphere of a-phase 239Pu metal is 10.3 kg
  A bare sphere consisting of 4.5 kg of a-phase 239Pu metal has a fraction critical of:
What is the keff of the 4.5-kg 239Pu bare sphere?

## Slide 22: Multiplication Factor Vs. Fraction Critical
  The critical mass of a bare sphere of a-phase 239Pu metal is 10.3 kg
  A bare sphere consisting of 4.5 kg of a-phase 239Pu metal has a fraction critical of:
What is the keff of the 4.5-kg 239Pu bare sphere?

## Slide 23: Multiplication Factor Vs. Fraction Critical
  The critical mass of a water-reflected sphere of a-phase 239Pu metal is 5.4 kg
  A water-reflected sphere consisting of 4.5 kg of a-phase 239Pu metal has a fraction critical of:
  What is the keff of the 4.5-kg 239Pu reflected sphere?

## Slide 24: Multiplication Factor Vs. Fraction Critical
  The critical mass of a water-reflected sphere of a-phase 239Pu metal is 5.4 kg
  A water-reflected sphere consisting of 4.5 kg of a-phase 239Pu metal has a fraction critical of:
  What is the keff of the 4.5-kg 239Pu reflected sphere?

## Slide 25: Multiplication Factor Vs. Fraction Critical
  The critical mass of a water-reflected sphere of a-phase 239Pu metal is 5.4 kg
  A water-reflected sphere consisting of 4.5 kg of a-phase 239Pu metal has a fraction critical of:
  What is the keff of the 4.5-kg 239Pu reflected sphere?

## Slide 26: Single unit methods
Fraction Critical
Core Density Conversion
Diffusion Theory (including buckling)

## Slide 27: Core Density Conversions – Applicability & Limitations
The core density conversion method relates a critical core with a known density to an equivalent critical core with another density
Applicability
  Fissile material systems with homogeneous composition;
  Density change is uniform, and
  Unreflected (bare) OR when the density of the core and reflector are changed by the same factor
  EXCEPTION: If the system is reflected
    For water-reflected spheres where the density of the reflector is not changed (use of special exponent)
Limitations of the Core-Density Conversions
  Not for systems that contain heterogeneities such as lumps of fuel or fuel rods in a reactor
  Not for solution systems where fissile concentration is changed
  The core-density relationships presented here will not work if the density changes are not uniform

## Slide 28
Basis for the Method
  If the linear dimension of an assembly is scaled inversely with a change in density, any neutron path from one region to another will scale in the same way
  If the materials of that system remain unchanged, then there is no overall change with the neutron interactions in that system
    Even though the dimensions of the system change, the relative number of neutrons that leak out of the system, that are absorbed, or that scatter remains the same
    The number and type of interactions will not change
Core Density Conversions – Applicability & Limitations
n
n

## Slide 29: Core Density Conversions – Dimensional and Mass Relationships
Fundamental Form
  x is the linear dimension
  ρ is the density
REMINDER: valid for unreflected systems or reflected where the reflector density change is the same as that of the core
x
xo

## Slide 30: Core Density Conversions – Dimensional and Mass Relationships
Spherical Geometry
  Fundamental formula raised to the third power:
  Volume is proportional to r3:
  Volume is equal to mass divided by density:
ro
r

## Slide 31: Core Density Conversions – Dimensional and Mass Relationships
Spherical Geometry, cont’d
  Simplified to most useful form:

## Slide 32: Core Density Conversions – Dimensional and Mass Relationships
Infinite Cylindrical Geometry
  Fundamental formula squared:
  Cross-sectional area is proportional to r2:
  Area is equal to mass per unit length divided by density:
ro
r

## Slide 33: Core Density Conversions – Dimensional and Mass Relationships
Infinite Cylindrical Geometry, cont’d
  Simplified to most useful form:

## Slide 34: Core Density Conversions – Dimensional and Mass Relationships
Infinite Slab Geometry
  Fundamental Form
  Thickness is equal to mass per unit area divided by density:
  Simplified to most useful form:
Mass per unit area is sometimes referred to as areal density

## Slide 35: Core Density Conversions for Reflected Systems
Spherical Geometry
  The following relationship can be used to determine the critical mass (mc) for a reflected system when the reflector density remains constant
    The exponent “s” is a look up value
    Exponent is denoted as “n” in some sources
  s (or n) is approximately constant over the range 0.5 ≤ ρ/ρo ≤1.0
    For reflected systems approaching infinite dimensions, the exponent approaches a value of 2 (the difference between a bare and reflected system has no particular meaning when infinitely large)
    For reflected systems of small dimensions, the exponent has a value of ~1.5 (small, unmoderated, cores)

## Slide 36: Core Density Conversions for Reflected Systems
LA-3366
  Figure 15 shows values of s for water-reflected spheres

## Slide 37: Core Density Conversions – Example 1
The bare spherical critical mass of a-phase 239Pu metal (density = 19.86 g/cm3) is 10,300 g
What is the bare spherical critical mass of d-phase 239Pu metal (density = 15.76 g/cm3)?

## Slide 38: Core Density Conversions – Example 1
The bare spherical critical mass of a-phase 239Pu metal (density = 19.86 g/cm3) is 10,300 g
What is the bare spherical critical mass of d-phase 239Pu metal (density = 15.76 g/cm3)?

## Slide 39: Core Density Conversions – Example 2
The water-reflected spherical critical mass of a-phase 239Pu metal (density = 19.86 g/cm3) is 5,400 g
What is the water reflected spherical critical mass of d-phase 239Pu metal (density = 15.76 g/cm3)?

## Slide 40: Core Density Conversions – Example 2
The water-reflected spherical critical mass of a-phase 239Pu metal (density = 19.86 g/cm3) is 5,400 g
What is the water reflected spherical critical mass of d-phase 239Pu metal (density = 15.76 g/cm3)?
-s

## Slide 41: Core Density Conversions – Example 2
The water-reflected spherical critical mass of a-phase 239Pu metal (density = 19.86 g/cm3) is 5,400 g
What is the water reflected spherical critical mass of d-phase 239Pu metal (density = 15.76 g/cm3)?

## Slide 42: Single unit methods
Fraction Critical
Core Density Conversion
Diffusion Theory (including buckling)

## Slide 43: Diffusion Theory
Applicability
  Method can be used to calculate material parameters (e.g. diffusion length) that can be used to determine kinf
  With material parameters, critical dimensions can be determined
  With a reference system, this method can be used to determine dimensions of another system in a different geometry that has same keff (i.e. equivalent leakage )
    sphere, cylinder, or slab are typical
  This method can be used for a wide variety of bare and reflected systems including both metal and solution systems
  WARNING: The mass or volume of equivalent systems in different geometries will not (necessarily) be the same

## Slide 44: Diffusion Theory
Time dependent, one-speed diffusion equation
Rate of loss of neutrons by leakage and absorption plus rate of production of neutrons through fission equals the net rate of gain of neutrons
Steady state form
B2 (or Bm2) is defined as the material buckling
NOTE: adjustments are needed for thermal systems to thermally average cross sections

## Slide 45: Diffusion Theory
Recall the four factor formula
Assume p (resonance escape probability) and ε (fast fission factor) are 1
Then
Substitute back into the diffusion equation
Steady state form (L is diffusion length)
Modified production term

## Slide 46: Diffusion Theory Example
Godiva I Critical Assembly
Spherical geometry, unreflected
93.5% enriched uranium metal
Density = 18.74 g/cm3
Calculate kinf and material buckling

## Slide 47: Diffusion Theory Example
NA × 10-24 cm2/b

## Slide 48: Diffusion Theory Example

## Slide 49: Geometric Buckling
The solution to the time dependent diffusion equation is a series of spatial eigenvalues
Solution for Slab Geometry
Higher order eigenvalues decay more rapidly
Given enough time, the flux will decay into the shape represented by the fundamental eigenvalue – this is geometric buckling (Bg2)
In order for a fissile system to be at steady state (k=1), the flux shape has to be constant, i.e. the fundamental mode:
Notes: [Rate of change in the number of neutrons in V] – [leakage of neutrons from V] + [rate of absorption of neutrons in V] = [rate of neutron production in V]
D = lambda_transport/3
Lambda_transport = 1/SIGMA_S*(1-2/3A) = 1/SIGMA_S*(1-mu) where mu = cosine of the scattering angle

## Slide 50
Geometric Buckling

## Slide 51: Buckling Conversions (Shape Conversions)
Table from
LA-14244-M

## Slide 52: Diffusion Theory Correction
Diffusion theory over predicts critical dimensions, so the extrapolation distance, d, is used to adjust dimensions
  The extrapolation distance, d, can be calculated by
  The extrapolation distance is also a look up value
    Many references available for the extrapolation distance: ARH-600, LA-10860-MS, LA-3366 (available from the NCSP website)
Extrapolation distance is sometimes denoted by λ or δ
Unreflected systems

## Slide 53: Extrapolation Distance Lookup
Table from LA-3366

## Slide 54: Buckling Example 1
Godiva I Critical Assembly
Spherical geometry, unreflected
93.5% enriched uranium metal
Density = 18.74 g/cm3
Calculate the critical radius (when assembled)

## Slide 55: Buckling Example 1
Extrapolation distance rearranged in terms of D
R = r + d
Recall that d (extrapolation distance) is 0.71÷Σtr and D (diffusion coefficient) is 1÷ (3Σtr)
Recall from diffusion theory example that material buckling was determined to be 0.0876 cm-2 and D 1.021 cm

## Slide 56: Buckling Example 1

## Slide 57: Buckling – Example Problem 2
Consider a well inside a glovebox 60 cm × 45 cm in area
239Pu powder is stored in this glovebox
Now consider the possibility that powder is washed into the well and mixed with water at a concentration of 100 g Pu/L
Calculate the critical height of this mixture with 1-inch water reflection

## Slide 58: Buckling – Example Problem 2
Buckling and Extrapolation Distance
ARH-600

## Slide 59: Buckling – Example Problem 2
Buckling parameters at 100 g Pu/L
  Material buckling (Bm2) – 0.0255 cm-2
  Extrapolation Length (λ) – 4.2 cm
Bg2 =
  a = 60 cm
  b = 45 cm
  Solve for c

## Slide 60: Buckling – Example Problem 2
Solution
0.0255 cm-2 = [π / (60+2*4.2)]2 + [π / (45+2*4.2)]2 + [π / (c+2*4.2)]2
c = 13.8 cm
Caution – do not forget to multiply λ by 2

## Slide 61: Array methods
Limiting Surface Density (NBN2)
Surface Density
Density Analog
Solid Angle

## Slide 62: Array Methods – Introduction
Limiting surface density method, NBN2
  Calculate the critical center-to-center (c-t-c) spacing of units of a given mass in a cubic array
  Accounts for up to 200 mm of water reflection
Surface density method
  Calculate the subcritical c-t-c spacing of units of a given mass in an array that is limited in one dimension
  Accounts for up to 155 mm of water reflection
Density analog method
  Calculate the subcritical c-t-c spacing of units of a given mass in a cubic array
  Accounts for up to 200 mm of water reflection
62

## Slide 63: Array Methods – Introduction
Solid angle method
  Developed as a quick, empirical means of evaluating interaction between small numbers of fissile units
    In terms of total solid angle, W
  Maximum acceptable keff of individual units a function of W
  Accounts for thick water reflection
63

## Slide 64: Array methods
Limiting Surface Density (NBN2)
Surface Density
Density Analog
Solid Angle

## Slide 65: Limiting Surface Density Method
Applicability
  Useful for determining the critical center-to-center spacing OR mass for fissile materials in arrays
  Spherical units
  ≥64 units (4×4×4 minimum)
  Cubic array configuration
Need to know
  Number of units in the array
  A characteristic constant (c2) that is a function of the material properties of the array and the reflection
  Critical mass of an unreflected sphere of the fissile material in the array
  Mass of the fissile material in each array unit OR center-to-center spacing
65

## Slide 66: Limiting Surface Density Method
Surface density, σ(m), is a parameter that represents fissile mass projected on a plane
Expressed in g/cm2
Total mass in a stack within the array
Projected on the “footprint” of that stack
This method utilizes two formulations for surface density
Recall areal density from core density conversion

## Slide 67: Limiting Surface Density Method
Required for criticality
67

## Slide 68: Limiting Surface Density Method
Total number of units × geometric buckling of a cubic array (NBN2)
nz is the number of units in the “z” direction
m is the mass of a single unit (kg)
an is the half-spacing in the array (cm)
c is 0.55 ± 0.18 (empirically determined)
N is the total number of units
Geometry Line

## Slide 69: Limiting Surface Density Method
c2 is a constant dependent on material properties (cm-2)
  Slope of the material line
  Dependent on array reflection
  Empirically determined
  LA-14244-M
m0 is the unreflected critical mass (grams or kg)
As spacing between units is decreased, σ(m) becomes larger
As spacing between units approaches infinity, σ(m) becomes infinitesimal and mass approaches the unreflected critical mass
Material Line
General Observations

## Slide 70: Limiting Surface Density Method
70

## Slide 71: Limiting Surface Density Method
71
Divide each σ(m) formulation by m and solve the equality

## Slide 72: Limiting Surface Density Example
4x4x4 Water-Reflected Array
76.2 cm (30” c-to-c spacing between units)
U (100) metal units
c2 = 1.806×10-3 cm-2
m0 = 45.68 kg
Determine unit mass for array criticality
72

## Slide 73: Limiting Surface Density Example
4x4x4 Water-Reflected Array
76.2 cm (30” c-to-c spacing between units)
U (100) metal units
c2 = 1.806×10-3 cm-2
m0 = 45.68 kg
Determine unit mass for array criticality
73

## Slide 74: Limiting Surface Density Example
4x4x4 Water-Reflected Array
76.2 cm (30” c-to-c spacing between units)
U (100) metal units
c2 = 1.806×10-3 cm-2
m0 = 45.68 kg
Determine unit mass for array criticality
74

## Slide 75: Limiting Surface Density Example
75
critical m=34 kg
Graphical Representation

## Slide 76: Limiting Surface Density Example
Determine keff if the unit mass in the array is 20 kg U(100)

## Slide 77: Limiting Surface Density Example
Determine keff if the unit mass in the array is 20 kg U(100)
Fraction Critical

## Slide 78: Limiting Surface Density Example
Determine keff if the unit mass in the array is 20 kg U(100)

## Slide 79: Limiting Surface Density Example
Determine keff if the unit mass in the array is 20 kg U(100)

## Slide 80: Limiting Surface Density Example
Determine keff if the unit mass in the array is 20 kg U(100)

## Slide 81: Array methods
Limiting Surface Density (NBN2)
Surface Density
Density Analog
Solid Angle

## Slide 82: Surface Density Method
Applicability
  Derived from limiting surface density relationships
  Useful for determining the subcritical center-to-center spacing OR mass for fissile materials
  Array configurations where the size of the array is controlled in one direction (infinite planar dimensions)
  Maximum keff for an individual array unit cannot be larger than 0.9
Need to know
  Fissile unit stack height
  Critical dimensions for an infinite water-reflected critical slab of the fissile material in the array
  Critical mass of an unreflected sphere of the fissile material in the array
  Mass of the fissile material in each array unit OR center-to-center spacing
82

## Slide 83: Surface Density Method
From the limiting surface density technique:
For an infinite planar array (N=∞)
where d is the spacing between units in the array (cm)
83

## Slide 84: Surface Density Method
equal to zero when f=0.73
Material Line
Factor out m0
Safety Margin: unit keff≤0.9 (fraction critical 0.73)

## Slide 85: Surface Density Method
As unit mass approaches zero, allowable surface density approaches:
Substitute this result in σ(m) formula [σ0= σ(o)]
σ0 is the surface density of the water-reflected infinite slab (g/cm2)
  Critical thickness × density
Another safety factor that limits the computed surface density to 54% of σ0 (precludes tight spacing of small units):
Caution: do not use c2×mo

## Slide 86: Surface Density Method
Equality
Solve for d
m in units of grams; d in units of centimeters

## Slide 87: Surface Density Method
Infinite Planar Array
87
Conservatively applied to a finite planar array

## Slide 88: Surface Density Method
Infinite planar arrays
The coefficient 0.54 precludes small units from attaining criticality
Individual units with a keff = 0.9 (73% of the critical mass) results in an infinite center-to-center spacing result
Provides a subcritical result for the center-to-center spacing
The coefficient so is the surface density of the critical water-reflected infinite slab (g/cm2)
88
Summary

## Slide 89: Array methods
Limiting Surface Density (NBN2)
Surface Density
Density Analog
Solid Angle

## Slide 90: Density Analog Method
Applicability
  Useful for determining the subcritical center-to-center spacing OR mass for fissile materials
  Cubic array configuration
  Maximum keff for an individual array unit cannot be larger than 0.9
Need to know
  Fissile unit stack height
  Critical dimensions for an infinite water-reflected slab of the fissile material in the array
  Critical mass of an unreflected sphere of the fissile material in the array
  Mass of the fissile material in each array unit OR center-to-center spacing
90

## Slide 91: Density Analog Method
Finite Cubic Array
20 cm water reflector
91

## Slide 92: Density Analog Method
From the limiting surface density technique:
For a large arrays (as N approaches ∞)
where d is the spacing between units in the array (cm)
92
Same geometry representation as surface density method

## Slide 93: Density Analog Method
Recall from the Surface Density Method:
Set both formulations of σ(m) equal to each other
Solve for d:
So far, no difference from Surface Density

## Slide 94: Density Analog Method
Similar to the surface density relationship
Include a factor (different from that used in surface density) that represents experimental and computational data for cubic arrangements
  2.1 in place of 0.54

## Slide 95: Density Analog Method
Finite cubic arrays
The coefficient 2.1 represents experimental and calculational data for cubic arrangements of fissile materials
Individual units with a keff>0.9 (73% of the critical mass) results in an infinite center-to-center spacing result
Provides a subcritical result for the center-to-center spacing
The coefficient so is the surface density of the critical water-reflected infinite slab (g/cm2)
95
Summary

## Slide 96: Array Methods Example Results/Comparison
What is the minimum center-to-center spacing of an array of 4,500 g Pu(5) metal ingots?
The SD and DA results do not provide a spacing that represents a keff of 1.0
  Obviously, the spacing results are conservative from a criticality safety perspective when compared to the code results
The LSD results do provide a critical, i.e., keff of 1.0, spacing result
Case | SD | DA | LSD | Code Result
2x2x2 |  | 26 cm | Not applicable | 15 cm
10x10x10 |  | 57 cm | 42 cm | 41.7 cm
100x100x100 |  | 182 cm | 136 cm | 137 cm
Infinite Planar Array (1 unit high) | 36 cm |  |  | 25 cm
96

## Slide 97: Array methods
Limiting Surface Density (NBN2)
Surface Density
Density Analog
Solid Angle

## Slide 98: Solid Angle Method
The basic idea behind this method is that the subcriticality of an array configuration depends on
  The keff of a single representative unit in the array, and
  The probability that a neutron leaking out of this unit will interact with (cause fission in) another unit in the array
The probability that a leaking neutron will interact with another unit in the array is dependent upon total solid angle, W, at the most central unit, by all other units in the array
Related anomalies underscore this effect
98

## Slide 99: Solid Angle Method
  The following conditions must be satisfied in order to apply the method:
    The keff of any bare unit shall not exceed 0.8
    Each unit shall be subcritical when completely reflected by water
    The minimum surface-to-surface separation between units shall be 0.3 m (12 inches), and
    The allowed solid angle, W, shall not exceed 6 sr
      .
      keff in this formula is the keff of the bare unit
99

## Slide 100: Solid Angle Method
100

## Slide 101: Solid Angle Method
101

## Slide 102: Solid Angle Method
102
Problem: We want to store nine “safe”-bottles of fissile solution in a 3-by-3 array with 2-foot edge-to-edge spacing
Question: What is the highest keff that each bottle can have as a single unit and still be subcritical in the array?
  Each bottle is 4-feet tall
  Each bottle diameter ½-foot

## Slide 103: Solid Angle Method
103

## Slide 104: Solid Angle Method
104

## Slide 105: Solid Angle Method
105

## Slide 106: Solid Angle Method
106

## Slide 107: Solid Angle Method
107

## Slide 108: Solid Angle Method
108

## Slide 109: Solid Angle Method
109

## Slide 110: Solid Angle Method
110
Question: What is the highest allowed keff?

## Slide 111: Solid Angle Method
111

## Slide 112: Solid Angle Method
112

## Slide 113: Solid Angle Method
113

## Slide 114: Solid Angle Method
114
  What else is required?

## Slide 115: Solid Angle Method
115
  What happens if we move the bottles closer together?

## Slide 116: Resources
LA-14244-M, Hand Calculation Methods for Criticality Safety – A Primer
LA-3366 (Rev), Criticality Control in Operations with Fissionable Material
LA-10860-MS, Critical Dimensions of Systems Containing 235U. 239Pu, and 233U (1986 Revision)
NCSET Module 8, Hand Calculations Part 1
TID-7016 (Revision 2), Nuclear Safety Guide
Website: http://ncsc.llnl.gov/ncspMain.html